## Slide 1
CNN_distribution
distributor
icproValidate
spiNNaker2Simulator
parserSplitter
The distribution strategies for QPE with/without DRAM and SpiNNaker2 with 144 Pes are realized in this library. It depends on icproValidate, parserSplitter and spiNNaker2Simulator.
Library icproValidate is used to validate if the split sheme from parserSplitter is valid. Moreover, it generate validation data for ICPRO.
Library parserSplitter is for the neural network parser and splitter. The split scheme can be verified by icproValidate.
Library spiNNaker2Simulator is the simulator of SpiNNaker2.

## Slide 2
distributor
icproValidate
parserSplitter
spiNNaker2Simulator
distributor gets split scheme from parserSplitter, then feeds the split scheme into icproValidate to get the data size for data transfer as well as for creating different tasks for PEs. Afterwards, distributor distribute the tasks into spiNNaker2Simulator.

## Slide 3
Type | File Name | Description
NoC | nocDataTransfer.py | Performance estimation of NoC (SpiNNaker2)
QPE-DRAM | qpeDramDistributorDataReuse.py | Distributor for CONV With data reuse, with operator fusion
 | qpeDramDistributorNoDataReuse.py | Distributor for CONV Without data reuse, without operator fusion Without data reuse, with Operator fusion
 | qpeDramDistributorFcFusion.py | Distributor for FC Without operator fusion With operator fusion
 | qpeDramRoofline.py | Roofline model
 | qpeDramDistributionResult.txt | Distribution result
SpiNNaker2 | spiNNaker2DistributorDataReuse.py | Distributor for CONV With data reuse, with operator fusion
 | spiNNaker2DistributorNoDataReuse.py | Distributor for CONV Without data reuse, without operator fusion Without data reuse, with Operator fusion
 | spiNNaker2DistributorFcFusion.py | Distributor for FC Without operator fusion With operator fusion
 | spiNNaker2DistributoNoneConvFc.py | Clock cycle estimation for layers, which are not CONV and FC
 | spiNNaker2Roofline.py | Roofline model
 | qpeDramDistributionResult.txt | Distribution result
 | overallClocksBarPlot.py | Overall clocks estimation for VGG-16 and Resnet-50
Comparison of QPE-DRAM and SpiNNaker2 | qpeSpiNNaker2Compare.py | Performance comparison between QPE-DRAM and SpiNNaker2
Performance report for different size of MAC arrays | SpiNNaker2HwCompareRoofline.py | Comparison of MAC arrays with different size
 | SpiNNaker2_MAC_half.pdf/SpiNNaker2_MAC_half.pptx | Performance report
Other | distributionGerneral.py | Parent class for all distributor
 | rooflineModel.py | Parent class for all roofline model
distributor

## Slide 4
icproValidate
File Name | Description
dataGenerator.py | Generator data or data size for ICPRO or distributor (considering the memory alignment)
splitSchemeValidate.py | Validate if the split scheme is valid

## Slide 5
Type | File Name | Description
Parser | nnModel.py | Interface for adding different kinds of layers; INPUT for parserSplitter
 | nnMemParser.py | Calculate the required memory size for each layer
 | nnParser.py / nnParserUpgrade.py | Parse network into multiple primitive operators
Splitter | actiLayerMapper.py | Mapping non-linearity operation into QPE/SpiNNaker2
 | convLayerMapper.py, convLayerMapperDecrease.py, convLayerMapperForSpiNNaker.py | Mapping convolution operation into QPE/SpiNNaker2
 | fcLayerMapper.py | Mapping matrix-multiplication operation into QPE/SpiNNaker2
 | matEleLayerMapper.py | Mapping matrix element-wise operation into QPE/SpiNNaker2
 | paddLayerMapper.py | Mapping padding operation into QPE/SpiNNaker2
 | poolLayerMapper.py | Mapping pooling operation into QPE/SpiNNaker2
 | quanLayerMapper.py | Mapping quantization operation into QPE/SpiNNaker2
Others | nnGeneral.py | Parameters and constants for parser and splitter
 | nn2SpiNNaker2.py | Mapping NN to QPE/SpiNNaker2; OUTPUT for parserSplitter
parserSplitter

## Slide 6
spiNNaker2Simulator
Type | File Name | Description
Component simulator | xxxSimulator.py | Simulator of xxx component; with data in every transferred packet. Deprecated in later development, because the simulation is very slow!
 | xxxSimulatorNoDataTran.py | Simulator of xxx component but without data in every transferred packet.
triblock QPE | triBlockQpeSimulatorProcess.py | Simulator with 9 QPEs and 1 DRAM, Inheriting processing class
SpiNNaker2 | spiNNaker2TriBlockSimulator.py | SpiNNaker2 simulator, creating 4 triBlockQpeSimulatorProcess process